## Slide 1: ICS 460 – Transport Layer
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Overview
Builds on the network layer
  network layer: end-to-end packet delivery using datagrams or virtual circuits
  transport layer: data transport across networks from a process on a source host (app) to one on the destination host with the desired reliability or quality independent of the physical networks in use
  the user of the transport layer is an application
TCP
IP
802.11
app
IP
802.11
IP
Ethernet
TCP
IP
Ethernet
app
Router
Host
Host

## Slide 3: Transport Layer need
Reason for existence
  Users have no control over network layer services
    run on routers which are operated by ISPs, etc.
    cannot solve service problems there (lossy network, crashes, etc.) or at lower layers
  Only option
    put another layer on top which is responsible for improved quality of service
  Benefits:
    can hide failures in the underlying network (for reliable models)
      Connectionless network: uses timeouts and retransmissions
      Connection-oriented network: if connection abruptly terminated, reestablish and resume
    hides complexity of underlying networking technology
      Applications are programmed to the Transport Layer services
      provides a uniform API that abstracts out the differences between specific networking technology in use (connectionless Ethernet or connection oriented WiMax)

## Slide 4: Overview
Encapsulation
  first layer whose data is not examined by nodes internal to the network
    routers and switches examine packets and frames
  Segments are encapsulated within packets, within frames
  Segments contain
    TCP header (control information) and a Payload (application data)
802.11
IP
TCP
App, e.g., HTTP
Segment
Packet
Frame

## Slide 5: Socket API - revisited
Simple abstraction to use the network
  The “network” API (really Transport Service) used to write all Internet apps
  Part of all major OSes and languages (originally BSD Unix 1983)
Supports both Internet transport services
  streams and datagrams
Lets apps attach to the local network at different ports
Socket,
Port #1
Socket,
Port #2

## Slide 6: Socket API
Same API used for both streams and datagrams
Only needed for Streams
To/From forms for
Datagrams

## Slide 7: Ports
Application process is identified by the tuple:
  { IP address, protocol, and port }
Ports
  16-bit integers representing local “mailboxes” that a process leases
Servers bind to well-known ports
  < 1048, requires admin privileges
  E.g., FTP:20, 21; SSH:22; SMTP:25; HTTP:80; HTTPS:443; etc.
Clients are assigned ephemeral ports
  chosen by the OS, used temporarily

## Slide 8: Transport Layer Services
  Provides two different data delivery/transport options
    Reliability dimension
      Unreliable:
        packets lost in the network are exposed to the transport’s user (the application)
      Reliable:
        packets can still be lost, but the transport layer handles it, so the application is unaware
    Data transfer dimension
      Message oriented: transfers self contained messages (like a post office)
      Bytestream: an infinite stream of bytes
    For the Internet, this layer provides
      TCP: a bidirectional reliable bytestream between applications
      UDP: a datagram model to send messages If an app wants reliable messaging (e.g., DNS), it must do the work itself
      Nothing between these extremes

## Slide 9: User Datagram Protocol (UDP)
UDP
  UDP is a glorified packet transporter (adds very little to the network layer)
    a datagram is just a packet
    messages can be lost/reordered/duplicated, have a limited size, and there is neither flow control nor congestion control
  used by apps that don’t want reliability or bytestreams
    VoIP (don’t want reliability)
    DNS (prefer message oriented exchanges)
    DHCP (for bootstrapping the network – prefer not to need complexity of TCP)
  if an application wants reliability using messages, it must implement it itself

## Slide 10: Datagram sockets
Client (host 1)
Server (host 2)
Time
1: socket
2: bind
1: socket
6: sendto
3: recvfrom*
4: sendto
5: recvfrom*
7: close
7: close
*= call blocks
request
reply
    client and server both have sockets
    server: bind it to a well known port
    server calls receiveFrom() –blocks until message arrives
    client calls sendTo() to send a message On server, recvFrom() unblocks and server retrieves the message
    client calls recvFrom() for the response
    server responds using sendTo() Client’s receiveFrom() unblocks and it processes the response
    Both call close() to tidy up
    Note: no connection needed

## Slide 11: UDP Header
  Ports identify sending and receiving application processes
    presence of ports is the key difference between just raw packets
    without ports, receiving layer would not know which application to send to
    with ports
      on receipt, its payload is handed to the process attached to the destination port
      source port is needed when a reply must be returned
  Datagram length of 8 byte header + payload (size limit of 65,515 bytes)
  16-bit checksum for reliability (optional)
    zero means no checksum

## Slide 12: UDP Header
  Checksum, if present, includes
    IP pseudoheader prepended to the UDP segment (UDP header + payload)
      also checks key IP fields (addresses) to detect misdelivered packets
      Not a layering violation, since the transport layer already knows these details

## Slide 13: UDP service
UDP provides
  a common interface to the IP protocol (Sockets)
  (de)mux of multiple processes (via ports) accessing the single network
  optional end-to-end error detection (via the checksum)
UDP does not provide
  flow control, congestion control, retransmission on receipt of a bad segment
  If application needs these, it must implement it in its own code
Best for client/server type applications (e.g., DNS)
  client sends a short request (lookup hostname), and server returns a short response (IP address)
  if either is lost, client times out and retries
  code is simple (no setup/tear down), and fewer messages than with TCP

## Slide 14: Transport Layer - Transmission Control Protocol
  TCP provides reliable end-to-end bytestream over an unreliable internetwork
    Bytes are delivered once, reliably, and in order;
    supports arbitrary length content
    Supports flow control (match sender to receiver) and congestion control (match sender to the network)
  TCP in the Transport layer
    accepts user datastreams from local processes
    breaks them up into pieces not exceeding 64KB (in practice 1460 data bytes to fit in an Ethernet frame)
    sends each piece as a separate segment
    Receiving layer reconstructs the original byte stream (reliably, in order)
  Connection oriented
    connection must be explicitly established between a socket on one host and a socket on another

## Slide 15: Transmission Control Protocol (TCP)
Reliable bytestream
  a TCP connection is a bytestream – not a message stream
  message boundaries are not preserved end-to-end
  if sender does four 512-byte writes, can be delivered as one 2048-byte chunk
    no way for receiver to detect the units in which the data were written
Four segments, each with 512 bytes of data and carried in an IP packet
2048 bytes of data delivered to app in a single recv() call
Sender
Receiver

## Slide 16: TCP – Reliable Bytestream
Bidirectional data transfer
  control information (ACKs) piggyback on data segments in reverse direction
    data segment from AB is also carrying an ACK for the reverse stream from BA
  Every byte on a TCP connection has its own 32-bit sequence number
  Segment consists of 20 byte header followed by 0+ data bytes
    Each segment must fit in the 65,515 byte IP payload
    each segment must fit in the link’s MTU (Ethernet: 1500 bytes)
A
B
data ba
ack ab
ack ba
data ab

## Slide 17: TCP Header
  Fixed Format 20-byte header
    16-bit Ports identify applications
    SEQ number, ACK number (next in-order byte expected, if ACK flag is set)
      cumulative ACK: summarizes the received data with a single number
      Both are 32-bits because every byte of data is numbered
    TCP Header length: needed because Options are of variable length
    Flags for congestion control, connection setup, etc.

## Slide 18: TCP Header
  Fixed Format 20-byte header
    Window size for flow control (relative to ACK, and in bytes)
      indicates the buffer space available at the receiver
      lets the receiver control how many bytes the sender may transmit
    Checksum of the header, data, and a pseudoheader (with protocol=6 for TCP)
    Options: lets each host specify the Maximum Segment Size it can accept, etc.

## Slide 19: TCP Connection Establishment
Sender and receiver must prepare for data transfer
  Signaling is used to agree on parameters (e.g., max segment size)
    segments that carry control information are exchanged
Three way handshake
  opens connection for data in both directions
  initiated by an active party (the client) on a passive party (the server)

## Slide 20: Three way handshake
  Server waits for an incoming connection
  Client executes a CONNECT with the IP address and port and parameters
  Process (happy path):
  Client sends TCP SYN segment with SYN=1, ACK=0, and picks ISN=x
  Server replies with SYN(y), a fresh ISN; and ACK(x+1), since SYN takes up 1 byte and we ACK the next expected byte (x+1)
  Client sends back SEQ=x+1, and ACK for y+1. The connection is now open.
  If either SYN is lost, it is retransmitted
  Side effect: both agree on sequence numbers to use for data (need not start at 1)
1
2
3
Active party
(client)
Passive party
(server)
SYN (SEQ=x)
SYN (SEQ=y, ACK=x+1)
(SEQ=x+1, ACK=y+1)
Time

## Slide 21: TCP Connection Release
  Releasing the connection
    delivers all pending data, and cleans up state in sender and receiver
  Two styles of connection release
    Asymmetric: any party can simply hang up to terminate the connection
      Problem: what if one party is sending data when the other abruptly hangs up?
    Symmetric: each party controls closing their own end of the connection
      each can continue to transmit data and close down when they are finished
      avoids data loss by ensuring that all pending data is delivered before connection is released
      but: connections can now be half-open, with one side closed, and the other is finishing up
  Either the client or the server could initiate closing of the connection
    which goes first depends on the application protocol

## Slide 22: TCP Connection Release
  Active sends FIN(SEQ=x), x is the current sequence number for that connection
    TCP segment with FIN bit set indicates no more data to send
  Passive ACKs(x+1) the FIN. Active endpoint is closed and cannot send new data
    Passive may continue to send data in the other direction
  Passive sends FIN(y)
  Active ACKs(y+1) the FIN
  when both directions are shut down, the connection is released
  FINs are retransmitted, if lost
Active party
Passive party
1
2
FIN (SEQ=x)
(SEQ=y, ACK=x+1)
(SEQ=x+1, ACK=y+1)
FIN (SEQ=y, ACK=x+1)

## Slide 23: Flow Control Overview
  Error Control: ensures that data is delivered without errors
  Flow Control: ensures that a fast sender cannot overrun a slow receiver
  Transport layer uses the same mechanisms as for the data link layer
    frame carries an error detecting code (checksum)
    Sliding window protocol
      Automatic Repeat reQuest (ARQ):
        frame carries a sequence number to identify itself,
        is retransmitted until it receives an ACK of successful receipt
      Stop and Wait
        sender allows only a max number of frames to be outstanding at any time.
      supports bidirectional data transfer

## Slide 24: Flow Control Overview
  mechanisms are the same, but:
    differ in function
      link layer checksum protects a frame as it crosses a single link
        valuable for performance (else a corrupt packet can be send along the entire path unnecessarily)
      transport layer checksum protects a segment as it crosses an entire network path: a faulty router can cause segments to be corrupted, even though they were correct according to the checks at each link
        end-to-end check is essential for correctness
    differ in degree
      most wireless links (eg. 802.11) have a low BD product, and so can use stop-and-wait
      TCP connections have high BD product that is much larger than a single segment, so it needs a large sliding window.

## Slide 25: Buffering inside the Transport Layer
  Used for
    arriving segments: wait until application calls receive()
    leaving segments: placed when application calls send()
  Port mux/demux uses port number to assign segments to the right queue
  Host may have many connections
    so may need substantial buffering

## Slide 26: Sliding Window - Receiver
  Modification to sliding window for receiver to slow an over enthusiastic sender
    In addition to pipelining to keep the network busy, wish to avoid overloading receiver
  Consider receiver with W buffers for out-of-order packets
    LAS = LAST ACK SENT, app pulls in-order data from buffer with recv()
    Suppose next 2 segments arrive but app is overwhelmed and does not call recv() LAS rises, but we can’t slide window!
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
seq. number
5
5
5
5
Acceptable
Sliding
Window
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
Acked

## Slide 27: Sliding Window - Receiver
  If further segments arrive, we can fill the buffer
    must drop segments until app calls recv()
  App recv() takes 2 segments – window slides!
    with a slow receiver, we could have lost packets
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Nothing
Acceptable
seq. number
5
4
4
Acked
4
4
4
Acked
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
4
Acked

## Slide 28: Flow Control
Avoid loss at receiver
  tell sender the available buffer space
  Flow control window (WIN) = #Acceptable, not W (measured from LAS)
  Sender uses lower of sliding window and flow control window (WIN) as the effective window size
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
Acked
..
5
6
7
5
2
3
..
LAS
WIN=3
Finished
3
..
Too high
seq. number
5
5
5
5
4
4
Acked

## Slide 29: Flow Control (TCP)
  Flow control with WIN: SEQ + length < ACK + WIN
  4KB circular buffer at receiver

## Slide 30: TCP Three Way Handshake
  Edge case:
    setup packets from a client were duplicated and delayed
    connection was established using original packets and ended
    delayed packets arrive
  Does not establish a connection:
    duplicate SYN(SEQ=x) arrives at the server
    Server sends SEQ=y, ACK=x+1
    client rejects this: it has not sent a SYN recently that corresponds to this ACK
    other (SEQ=1, ACK=z+1) arrives at the server
    Server rejects it as the ACK number is not the expected y+1
    Requires different ISNs to be picked each time
Active party
(client)
Passive party
(server)
SYN (SEQ=x)
SYN (SEQ=y, ACK=x+1)
(SEQ=x+1,
ACK=z+1)
X
X
REJECT
REJECT

## Slide 31: TCP Connection state machine
  Finite State machine captures states (rectangles) and transitions (arrows)
    A/B means
      event A triggers the transition (e.g., a socket API being called, or a packet arriving)
      the action B is done in response to the trigger (e.g., a SYN packet is sent)
  useful tool to specify and check the handling of all cases that may occur
  both client and server run their own independent instance of this FSM
    Client side is shown using solid lines, and Server side shown using dashed lines

## Slide 32: TCP Connection state machine – Client instance
  Client starts in CLOSED state (Active party)
    Transition event=call CONNECT, action=send SYN. New state=SYN SENT
  Client is in SYN SENT state
    event=SYN+ACK arrives from Server, action=send ACK. New state=ESTABLISHED

## Slide 33: TCP Connection state machine – Server instance
  Server starts in CLOSED state (Active party)
    event=call LISTEN. action=<none>. New state=LISTEN (wait for incoming call)
  Server is in LISTEN state
    event=SYN arrives from Client. action=send SYN+ACK. New state=SYN RCVD
  Server is in SYN RCVD state
    event=ACT from Client. action=<none>. New state=ESTABLISHED

## Slide 34: TCP Connection State Machine – Client Instance
  Client is in ESTABLISHED state (Active party)
    event=call CLOSE. action=send FIN. New state=FINWAIT1 (wait for ACK)
  Client is in FIN WAIT 1 state
    event=ACK from Server. action=<none>. New state=FIN WAIT 2
    Client end of connection is closed, and all state is cleaned up
  Client is in FIN WAIT 2 state
    event=FIN. action=ACK. New state=TIME WAIT
    gives time for resend of FIN, if our ACK was lost
  Client waits for timeout, and goes to CLOSED
    waits for straggling packets to arrive before closing the connection

## Slide 35: TCP Connection State Machine – Server Instance
  Server is in ESTABLISHED state (Passive party)
    event=receive FIN. action=send ACK. New state=CLOSEWAIT1
    the transport layer waits for the application to realize that this is a closed connection
  Server is in CLOSE WAIT state
    event=call CLOSE. action=send FIN. New State = LAST ACK
    application realizes that the connection is closed, and issues a CLOSE call
  Server is in LAST ACK
    event=ACK received. action=<none> New state=CLOSED