## Slide 1: ICS 460 – Application Layer
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Application Layer
  Builds distributed “network services” (DNS, Web) on Transport services
  Application layer protocols are often part of an “app”
TCP
IP
802.11
HTTP
app
OS
User-level
(NIC)

## Slide 3: DNS
  DNS (Domain Name System)
    Naming service to map between host names and their IP addresses
      www.uwa.edu.au  130.95.128.140
    Human-readable names
      Names are higher-level identifiers for resources
      Addresses are lower-level locators for resources
      Resolution (or lookup) is mapping a name to an address
  Goals:
    Easy to manage (esp. with multiple parties)
    Efficient (good performance, few resources)
  Approach:
    Distributed directory based on a hierarchical namespace
    Automated protocol to tie pieces together
www.uw.edu?
Network
128.94.155.135

## Slide 4: Top Level Domains (TLDs)
  Run by ICANN (Internet Corp. for Assigned Names and Numbers)
  22+ generic TLDs
    Initially .com, .edu , .gov., .mil, .org, .net
    Added .aero, .museum, etc. from ’01 through .xxx in ’11
    Different TLDs have different usage policies
  ~250 country code TLDs
    Two letters, e.g., “.au”, plus international characters since 2010
    Widely commercialized, e.g., .tv (Tuvalu)
    Many domain hacks, e.g., instagr.am (Armenia), goo.gl (Greenland)

## Slide 5: DNS Namespace
  Hierarchical, starting from “.” (dot, typically omitted)
  A zone is a contiguous portion of the namespace
    basis for distribution
      EDU registrar administers .edu
      UW administers washinton.edu
      CS&E administers cs.washington.edu
A zone
Delegation

## Slide 6: DNS Namespace
  Each zone has a nameserver to contact for information about it
    Zone must include contacts for delegations, e.g., .edu knows nameserver for washington.edu
    is comprised of DNS resource records that give information for its domain names
      A record: IPv4 address of a host
      CNAME record: alias name
      NS record: nameserver of domain or delegated subdomain
A zone
Delegation

## Slide 7: DNS Mechanics
  Originator (filts.cs.vu.nl) wants to resolve robot.cs.washington.edu Assume: local NS uses recursive query, and does not know robot’s IP address
  originator queries its local name server (a configured address)
  local name server begins at the root name server
  root server does not know robot, but replies with the NS of .edu
  local name server contacts .edu NS for robot.cs.washington.edu

## Slide 8: DNS Mechanics
  .edu’s NS does not know robot, but replies with NS for washington.edu
  local name server contacts washington.edu NS for robot
  washington.edu’s NS does not know robot, but replies with NS for cs.washington.edu
  local name server contacts cs.washington.edu for robot
  cs.washington.edu’s NS returns the IP address for robot.
  local NS returns the IP address to originator

## Slide 9: Web
HTTP request
HTTP response
Page as a set of related HTTP transactions

## Slide 10: Web Protocol
  HTTP is a request/response protocol for fetching Web resources
    Runs on TCP, typically port 80
    Part of browser/server app
TCP
IP
802.11
browser
HTTP
TCP
IP
802.11
server
HTTP
request
response

## Slide 11: Fetching a Web page with HTTP
  Start with the page URL:
  http://en.wikipedia.org/wiki/Vegemite
  Steps:
    Resolve the server to IP address (DNS)
    Set up TCP connection to the server
    Send HTTP request for the page
    (Await HTTP response for the page) **Execute / fetch embedded resources / render
    Clean up any idle TCP connections
Protocol
Page on server
Server

## Slide 12: Static vs Dynamic Web pages
  Static web page is a file contents, e.g., image
  Dynamic web page is the result of program execution
    Javascript on client, PHP on server, or both

## Slide 13: HTTP Protocol
  Request commands
Fetch
page
Upload
data

## Slide 14: HTTP Protocol
  Codes returned with the response
Yes!

## Slide 15: HTTP Protocol
  Many header fields specify capabilities and content
    E.g., Content-Type: text/html, Cookie: lect=8-4-http

## Slide 16: HTTP Performance
  Page Load Time
    key measure of web performance
    time from click until user sees page
  Ways to decrease PLT:
    reduce content size for transfer (smaller files, compression)
    change HTTP to make better use of available bandwidth
    caching/proxies to avoid repeated transfer of the same content
    move content closer to the client (CDNs)

## Slide 17: Persistent Connections
  Parallel connections: browser runs multiple HTTP instances in parallel
    but connections compete with each other for network resources
  Persistent connections: use 1 TCP connection for multiple HTTP requests
  Pipeline requests (optional)
One request per connection
Sequential requests per connection
Pipelined requests per connection

## Slide 18: HTTP Web Caching
  Users often revisit web pages
    Big win from reusing local copy!
  How to determine if local copy is still valid?
Network
Cache
Local copies
Server

## Slide 19: Web Caching
  Locally determine copy is still valid
    Based on expiry information such as “Expires” header from server
    Or use a heuristic to guess (cacheable, freshly valid, not modified recently)
    Content is then available right away
  Revalidate copy with remote server
    Based on timestamp of copy such as “Last-Modified” header from server
    Or based on content of copy such as “Etag” header from server
    Content is available after 1 RTT
Network
Cache
Server
Network
Cache
Server

## Slide 20: Web Caching
  Putting the pieces together:

## Slide 21: Web Proxies
  Place intermediary between pool of clients and external web servers
    Clients benefit from
      larger, shared cache
      security checking,
      enforces organizational access policies
    Benefits limited by secure / dynamic content, as well as “long tail”
  Clients contact proxy; proxy contacts server
Cache
Near client
Far from client