## Slide 1: ICS 460 – Physical Layer
2019
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Scope of the Physical Layer
Lowest layer in the protocol model
  Goal is to convey bits across a physical channel (e.g., wires, air)
  But:
    A physical channel only carries analog signals
    we need a way to represent bits using analog signals
…10110
10110…
Signal

## Slide 3: Simple Link Model
  Channel’s physical properties determine
    Performance
      Rate (bandwidth, capacity, speed, throughput) in bits/second rate at which bits can be sent across the channel
      Delay (latency) in seconds, time taken for a signal to cross the physical channel
      Error rate number of bits that arrive garbled (very high for wireless channels)
  Other properties:
    Whether broadcast or point-to-point
    cost, ease of installation, and maintenance
Delay D, Rate R
Message

## Slide 4: Message Latency
Latency is the delay to send a message over a link:
  Transmission delay: time to put M-bit message “on the wire”
    T-delay = M (bits) / Rate (bits/sec) = M/R seconds
  Propagation delay: time for bits to propagate across the wire
    P-delay = Length / speed of signals in the medium
    = Length / ⅔c ... use c for wireless; 2/3 c for wires = D seconds
  Combining the two terms we have: L = D + M/R

## Slide 5: Metric Units
The main prefixes we use:
Use powers of 10 for rates, 2 for storage
  1 Mbps = 1,000,000 bps, 1 KB = 210 bytes
“B” is for bytes, “b” is for bits
Prefix | Exp. | prefix | exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9

## Slide 6: Latency Examples
Dialup modem link within a city (short distance over a slow link):
  R = 56 kbps, M = 1250 bytes D = 5 ms ... short link, with a small propagation delay
  L = D + M/R = 5 ms + (1250x8)/(56 x 103) sec = 5 ms+ 179 ms= 184 ms
Broadband cross-country link (long distance over a fast link):
  R = 10 Mbps, M = 1250 bytes ... fast link D=50ms ... long link, with a large propagation delay
  L = 50 ms + (1250x8) / (10 x 106) sec = 51 ms
A long link or a slow rate means high latency

## Slide 7: Bandwidth-Delay Product
Intuition: messages take up space on the wire
  sender has dropped bits in one end, but have not arrived yet at the receiver
  appear as if “stored” in the wire – just like drops of water in a pipe
Amount of stored data is the bandwidth-delay product
  BD = R x D
  Measure in bits, or fractions of messages or packets
  Small for LANs (e.g., wifi), big for “long fat” pipes (e.g., 1 Gbps cross country link)

## Slide 8: Bandwidth-Delay Product Example
Fiber at home, cross-country
  R=40 Mbps, D=50 ms
  BD = 40 x 106 x 50 x 10-3 bits
  = 2000 Kbit
  = 250 KB
a lot of data “in the network”!
110101000010111010101001011

## Slide 9: Types of Media
Media propagate signals that carry bits of information
categories of media
  guided (wires, fiber optic or coaxial cable)
  unguided (wireless)

## Slide 10: Wires – Twisted Pair
    Most common; used in LANs and telephone lines. Can run for long distances.
    Bandwidth depends on the thickness of the wire and the distance traveled.
    Twisting
      cancels out electrical interference produced by adjacent wires (crosstalk)
      reduces tendency of wire to act as an antenna
    Shielding
      Unshielded: 4 pairs of wires, relies on twisting for protection
      Shielded: adds shielding around each pair, and around the entire cable for added protection. More expensive.
    Advantages: provides high bandwidth at a low price and is easy to install.
Category 5 UTP cable with four twisted pairs

## Slide 11: Wires – Twisted Pair
    Cat ratings describe shielding as well as twists per meter
      as shielding and twists go up, so does cost, and overall diameter (volume/weight/flexibility)
      CAT3: used for older 10Mbps networks and telephone lines
      CAT5: supports 1Gbps up to 100m. Increased twists for better quality signal
        CAT 5E revised standard to fixes problem with CAT 5.
      CAT6/CAT6A: adds more twists/m and a central divider barrier, to support up to 10Gbps
        CAT 6A: supports 10Gbps over a longer distance. Twists wires into double helix configuration.
      CAT7: Shielded Twisted Pair
    Terminated using RJ45 jacks
    Come in 3 types
      Riser: used for standard patch cables, as well as in cabinets and racks
      Plenum: releases fewer toxins when burned, so can be used in space that circulates air
      Outdoor: thicker jacketed and UV protected.
Category 5 UTP cable with four twisted pairs

## Slide 12: Wires – Coaxial
    Termed coaxial because it has two conductive materials centered around a single axis
      stiff copper wire is surrounded by insulation, encased in a braided mesh conductor
    Rated on a system called "radio guide" (RG).
      "RG“ number loosely determines center conductor size (RG6 is commonly used.)
    Coaxial cables for data uses a compression- or crimp-style BNC connector.
    Bandwidth depends on cable quality and length.
    Advantages
      construction and shielding give it high bandwidth and excellent noise immunity.
      Coaxial cables have been replaced by fiber on long haul routes.

## Slide 13: Wires – Fiber Optics
    Long, thin strand of glass
    light from one end (LED or laser), bounces until it comes out the other end
    detected at the other end by a photodetector
    Enormous bandwidth over long distances (100km+) with low attenuation
    Types
      multi-mode (shorter links, cheaper) – multiple light rays at different angles
      single-mode (up to ~100 km at 100Gbps): light propagates in a straight line without bouncing
    Construction
      center glass core surrounded by glass cladding that keeps all the light in the core.
      plastic jacket protects the cladding.
      Fibers are grouped in bundles, protected by an outer sheath.
Light source
(LED, laser)
Photo-detector
Light trapped by
total internal reflection
Optical fiber

## Slide 14: Wires – Fiber Optics
    Some connectors
      ST connector – oldest type, BNC-like punch in and twist operation
      SC (standard Connector) – a snap-in connector
      FC (Ferrule Connector) – threaded-on. Replaced by SC and LC
      LC (Lucent Connector): small form factor (half the size of SC)
      LC to LC patch cable, duplex

## Slide 15: Wires – Fiber Optics
    Advantages
      bandwidth available is very large (many GHz)
      low attenuation – so fewer repeaters needed
      not affected by EMI, power surges, etc.
      thin – so needs less capacity in ducts
      light – reducing the cost of mechanical support systems 1000 UTP 1 km long weighs 8000kg. 2 fibers have more capacity and weighs 100 kg.
      difficult to wiretap
    Disavantages
      easily damaged by being bent too much
      essentially unidirectional – so duplex communication requires 2 fibers (e.g., LC-to-LC duplex)
      fiber interfaces cost more

## Slide 16: Wireless
Sender radiates signal over a region
  In many directions, unlike a wire, to many receivers
  Advantage: can reach many different receivers at the same time
  Drawback: signals from nearby transmitters sent on the same frequency, interfere at a receiver; which can garble messages. Hence must coordinate how the wireless spectrum is used.

## Slide 17: Wireless – US Frequency Allocation chart
Government allocates frequencies to radio, TV, police bands, aircraft, and computer communications
  Wifi uses the ISM frequencies (unlicensed – no license fees)
  But: computers using these frequencies must coordinate amongst themselves (the government is not explicitly allocating us a frequency)
  And: must compete with other devices (e.g., cordless phones)
802.11
b/g/n
802.11a/g/n

## Slide 18: Wireless – 802.11 modes
  Infrastructure mode:
    Basic Service Set: WAP and its associated stations – identified by a Service Set ID
      WAPs broadcast a wireless signal and are connected to a wired network
      Each WAP and its clients communicate on a single channel
    Extended SSID:
      Multiple connected BSS’
      Several WAPs can be connected by a wired network called a distribution system
      Connect WAPs to same switch, and use same SSID, for campus-wide access
  Ad hoc mode
    Not common. Clients directly send frames to each other - no WAP/Distribution System

## Slide 19: Wireless – 802.11 Standards
  802.11 Wifi, 1997: ran at 2Mbps.
  802.11b, 1999: ran at 11 Mbps on the 2.4GHz ISM band
  802.11a, 1999: ran at 54Mbps on the 5GHz ISM band
  802.11g, 2003: ran at 54Mbps on the 2.4GHz band
    backwards compatibility with 802.11b
  802.11n, 2009: multiple input/multiple output (MIMO) uses multiple antennas between WAP and client at the same time.
  802.11ac: 1Gbps. MU-MIMO - WAP uses its multiple antennas to transmit to multiple clients simultaneously.
    Multiple clients cannot send to the WAP at the same time
    Speeds up downloads

## Slide 20: Topology
    Bus topology
      oldest network technology - each node connects to a single backbone cable (bus)
      if one node sends data, everyone else hears it, and either process it or throw it away
      requires a way to detect/avoid collisions
    Ring topology
      all nodes connect to a single backbone cable, and cable is connect to itself – as a ring
      Token is passed around the network, giving each node a chance to send a signal
      Heavy traffic can slow it down
    Hierarchical Star topology
      all nodes connect to a central switch
      more expensive than bus – needs more cables
      BUT damaged cable will not bring down the entire network, and is easy to troubleshoot
      central switch is a SPoF, but easy to troubleshoot
    Point to Point topology
      two nodes directly interconnected with no intervening device (two sites in a WAN connected over a dedicated leased line, or virtual connection over the Internet)

## Slide 21: Signals - Frequency Representation
Fourier analysis
  A signal can be represented by an infinite number of sine waves of a fundamental frequency and its harmonics
weights of harmonic frequencies
Signal over time
=

## Slide 22: Signals - Frequency Representation
Fourier analysis
weights of harmonic frequencies
Signal over time
=
amplitude

## Slide 23: Signals - Effect of Less Bandwidth (EE)
every channel attenuates the signal
  if all components equally diminished, resulting signal is reduced in amplitude but not distorted
  BUT different harmonics are attenuated by different amounts
  Wire transmits up to cutoff frequency - its “bandwidth” (overloaded term!!!); higher frequencies are attenuated
Lost!
Lost!
Lost!
Bandwidth

## Slide 24: Signals - Effect of Less Bandwidth (EE)
  Goal: retain a signal with just enough fidelity to reconstruct the bits sent
    for networks, 8 harmonics are sufficient; additional fidelity is wasteful
    for hifi stereo, need higher bandwidth signal to retain additional harmonics
  Key Idea: fewer frequencies degrade the signal by making it more rounded
Lost!
Lost!
Lost!
Bandwidth

## Slide 25: Signals over a Wire
What happens to a signal as it passes over a wire?
  The signal is delayed (propagates at ⅔c)
  The signal is attenuated (goes for m to km)
  Frequencies above a cutoff are highly attenuated
  Noise is added to the signal (later, causes errors)

## Slide 26: Key channel properties: Bandwidth (EE)
Transmitted Signal bandwidth (EE)
  Analog Bandwidth
    range of frequencies present in the signal (measured in Hz)
    width of frequency band (in Hz) that wire allows without significant attenuation
  a physical property of the channel
    depends on construction, thickness, and length
  Impact
    Limits the rate of transitions
    determines Digital Bandwidth (CS), Channel Capacity, Maximum Data Rate (bps)
      larger the range, the quicker the signal transitions, and conveys more information. E.g., doubling the fundamental frequency, doubles the data rate
  But:
    cannot increase signal bandwidth indefinitely – data rate is limited by noise

## Slide 27: Fundamental limits
  Information is conveyed by change in value of the signal over time
    Change of value over time == frequency
    sharper transitions are a function of the width of the band of frequencies in a signal
    I.e., to double data rate, double the signal bandwidth
  BUT
    cannot increase signal bandwidth indefinitely – link and standards limit bandwidth
  Achievable data rate is limited by Link’s bandwidth + Noise at the receiver
  Nyquist theorem, 1924 – only consider link’s bandwidth
    max data rate (capacity), C = 2B transitions/sec = 2B log2V bits/sec
      2B samples per second
      V different transition levels (symbols) per sample – or, bits encoded into each transition
    a noiseless link of bandwidth B only permits frequencies up to 2B transitions/second
    I.e., higher frequencies are filtered out, so no point in sampling > 2B times/sec
    For a 3KHz channel, with binary signaling, C = 6Kbps. Link cannot transmit faster

## Slide 28: Fundamental Limits: Nyquist theorem
Max data rate for a noiseless channel of bandwidth B Hz
  C = 2B symbols/sec (baud rate) = 2 B log2 V bits/sec (bit rate) = 2B (if V=2)
    V is the number of symbols (represents 1+ bits)
  Converse: to achieve transmission rate of 2B symbols/sec, the channel must allow signals with frequencies up to B Hz.
Implications
  In theory, increasing V, increases C.
    I.e., by increasing V infinitely, we could infinitely increase channel capacity, C
  In practice, V is limited by the SNR

## Slide 29: Key Channel Properties: SNR
Strength of Signal and Noise at the receiver
  Number of different signaling levels (symbols) we can distinguish
  depends on relative strength of the signal to the noise
    Higher the SNR, the more levels we can distinguish
    Here we can distinguish 4 different levels
      even if noise muddies our signal, we can still reconstruct the actual value as long as the noise does not shift it so that it looks like a different symbol
Bandwidth B
Signal S,
Noise N
0
1
2
3
N
S+N

## Slide 30: Fundamental Limits: Shannon’s theorem
Max data rate for a noisy channel of bandwidth B Hz depends on received power (SNR):
  C = B log2 (1+S/N) bits/sec, where SNR is in decibels as 10*log10(S/N)
    SNR of 10 is 10dB, 100 is 20dB, and 1000 is 30dB, etc.
  Example:
    for ADSL: B=1MHz; SNR=40dB for short lines (1-2km) C = 1*106*log2(1+10000) = 13.3*106 = 13.3 Mbps.
    for a typical phone line (SNR of 30dB and B=3khz): C=3*103* log2(1+1000) = 30 kbps (approx.)
  Implications
    To increase capacity of a channel.
      not possible to simply infinitely increase V (line encoding technique)
      we need more bandwidth OR must improve SNR

## Slide 31: Engineering to the fundamental limits
Wires, and Fiber
  Can design the link for a certain data rate
    bandwidth of the wire is fixed by the quality of the wire
    SNR is controlled by limiting the link to a certain length (limits attenuation)
Wireless
  Might be able to fix the bandwidth,
  But SNR can vary greatly: up to 60 dB (a factor of 1 million!)
    depends on distance of client from the Access Point
    cannot design the system for worst case, or we’ll always run at a slow rate
    Instead, must dynamically update the data rate to actual conditions

## Slide 32: Signals over Wireless
Multipath fading
  signals are reflected so multiple echoes reach a receiver along different paths
    receiver sees a superimposed signal
    some add to get a stronger signal, others cancel each other out for a faded signal
  difficult to deal with – can change within a very small distance (cms)
  solution: transmit along multiple independent paths

## Slide 33: Signals over Wireless
Spatial reuse
  Different senders may transmit on the same frequency
    a receiver will see superimposed signals - which interfere with each other
  But, signal attenuates faster than 1/dist2
    leads to the idea of spatial reuse (of the same frequency)
    transmitters can reuse the same frequency as long as they are far enough spatially
Signal
strength
Distance
A
B
C
Interference
No interference

## Slide 34: Modulation
Representing digital bits using analog signals
  This is the topic of modulation
    channels carry analog signals, continuously varying voltage or light intensity
    signal encodes 1s and 0s using a modulation sheme
      wires use positive and negative voltage
      optical fiber uses presence and absence of light
…10110
10110…
Signal

## Slide 35: Modulation
Baseband modulation
  signal bandwidth occupies 0 to B Hz.
  signal is sent directly on the medium (e.g., over a wire)

## Slide 36: Baseband modulation - Non Return to Zero
Sender represents 1 and 0
Receiver decodes the signal
  maps the signal samples to closest symbols

## Slide 37: Baseband modulation - Bandwidth Efficiency
To run NRZ faster, we need either
  more bandwidth
    but bandwidth is a limited resource
  use more than two signaling levels
    with 4 signaling voltages (V=4), each symbol represents 2 bits at once
    reduces the bandwidth needed
    works if the signal at the receiver is strong to distinguish the 4 levels
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1

## Slide 38: Baseband modulation - Clock Recovery
For all modulation schemes
  Receiver must know when one symbol ends and the next begins
  Receiver needs frequent signal transitions to decode bits
  With NRZ, a long run of 0s or 1s leaves the signal unchanged, making it hard to work out how many there are
Strategy
  introduce frequent transitions in the signal itself – Manchester encoding

## Slide 39: Baseband modulation - Manchester encoding
  clock runs at twice the bit rate ,so it makes a transition in every bit time
  XOR the data signal with a clock signal
    When XORed with the 0 level, it makes a low-to-high transition
    When XORed with the 1 level, it makes a high-to-low transition
  Downside: requires twice as much bandwidth as NRZ (a scarce resource)

## Slide 40: Baseband modulation - Clock Recovery – 4B/5B
Every 4 bits is mapped into a 5-bit pattern
  uses a fixed translation table
  0000  11110, 0001  01001, 1110  11100, … 1111  11101
  5-bit pattern is chosen so there will be at most 3 zeros in a row
  adds 25% overhead, but better than 100% overhead of Manchester encoding
  But: it does not prevent long runs on 1s
    can use NRZ Inverted to invert the signal level on a 1
    Code a 1 as a transition and 0 as no transition – fixes long runs of 1s
Coded Bits:
Signal:
1 1 1 0 1 1 1 1 1 0 0 1 0 0 1
Data Bits:
1 1 1 1 0 0 0 0 0 0 0 1

## Slide 41: Passband Modulation
Passband modulation
  for fiber or wireless, can’t use baseband modulation.
  must encode it onto a carrier signal that is operating at a higher frequency
    size of an antenna must be a fraction of the signal wavelength
    multiplexing by frequency band allows multiple signals to coexist on the channel
  carrier signal is simply a signal oscillating at a given frequency
  carrier signal (amplitude, frequency, phase) is modified to convey the signal
  Arbitrary band of frequencies is used to pass the signal
    Baseband signal is shifted to occupy a passband of S to S+B Hz
    does not change the information carried, but changes how it looks
    receiver shifts it back to baseband

## Slide 42: Passband Modulation
NRZ signal of bits
Amplitude shift keying
Frequency shift keying
Phase shift keying

## Slide 43: Multiplexing
Sharing of a link’s bandwidth across users
  costs the same to install a high bandwidth line as a low bandwidth line
  multiplexing shares each line among many signals

## Slide 44: Time Division Multiplexing
  Sharing over time
    users take turns over a fixed schedule (round robin)
      comparable to pairs of people in a room taking turns speaking
    each user gets the full bandwidth of the link for a small amount of time
      they get no bits for a while, while the others send
      while they send, they send at the max rate
    aggregate stream runs at the sum rate of the individual streams
    complicated: requires synchronization of when to send
      small guard time intervals accommodate small timing variations
    widely used in telephone and cellular networks

## Slide 45: Frequency Division Multiplexing
  uses passband transmission to share a channel
    spectrum is divided into frequency bands
    each user uses one band to send their signal – simultaneously
      pairs of people speak at different pitches, so each pair can converse simultaneously
    width of each frequency band limits the data rate for each user
      users send in parallel; user has same (but lower) bit rate for entire duration
    guard band keeps the channels separated (though does not eliminate noise)
    E.g., multiple AM radio stations transmit simultaneously in a 1MHz spectrum band

## Slide 46: Digital multiplexing
TDM and FDM are not effective for network traffic
  both are used to statically divide bandwidth of a link
    well suited if traffic is continuous, with relatively fixed number of users
    TV or radio stations always transmit, but in parallel on their assigned frequencies

## Slide 47: Digital multiplexing
Network traffic uses statistical multiplexing
  Network traffic is bursty (on/off source)
  one page request gets lots of packets, then no load while you read the page
  multiplex traffic based on the demand each user is placing on the link
    we use multiple access schemes to let users share access to a link
    whenever they need to send a packet, they get to send it
    this gives us the benefits of statistical multiplexing
      share network bandwidth dynamically based on statistics of demand rather than static allocation (as with TDM or FDM)

## Slide 48: Putting it all together – DSL
Digital Subscriber Line (DSL)
  widely used for broadband
  offer tens of Mbps
  Reuses twisted pair telephone line to the home
    wire has ~2 MHz of bandwidth but voice uses only lowest ~4 kHz

## Slide 49: DSL
DSL uses passband modulation (called OFDM)
  Separate bands for upstream and downstream (larger)
  Modulation varies both amplitude and phase (called QAM)
  High SNR: up to 15 bits/symbol; low SNR: only 1 bit/symbol
Upstream
Downstream
26 – 138
kHz
0-4
kHz
143 kHz to 1.1 MHz
Telephone
Freq.
Voice
Up to 1 Mbps
Up to 12 Mbps
ADSL2: