## Slide 1: ICS 460 – Data Link Layer
2017
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Data Link Layer
  Implementation
    Physical Layer process and some of the Data Link Layer process runs on hardware - firmware on a Network Interface Card
    Rest of the Data Link Layer process (device driver) and the Network layer process run as part of the OS

## Slide 3: Scope
Physical layer
  delivers a stream of bits over a link
  uses modulation to turn signals into a bit stream
  for a noisy link (wireless), adds extra bits (e.g., 4B/5B) to reduce errors
    but errors can still occur and must be detected/corrected by the next upper layer

## Slide 4: Functions
  Provides a well defined service interface to the network layer
    delivers a sequence of messages (frames) over the physical layer
    encapsulates network layer packets in frames
  Deals with transmission errors (esp. on lossy links)
    breaks up bit stream into discrete frames – using framing techniques
    performs error detection/correction (checksums, etc.)
    handles errors (correct error, or discard and notify)
  Flow control

## Slide 5: Framing
  Technique to delimit the start/end of frames
  Two techniques
    delimit using symbols that cannot occur in the data
      Physical layer helps with delimiting frames in Ethernet and 802.11
      4B/5B encoding maps 16 symbols into 32 symbols (for sufficient bit transitions)
      we use symbols that cannot occur in the data for framing

## Slide 6: Framing – Byte Count
    delimit using symbols that can occur in the data
      Byte count (motivational only)
        relies on a header field with a number of bytes
        receiver reads that many bytes for that frame
        BUT – no way to resynchronize after bit errors in the counter field

## Slide 7: Framing – Byte Stuffing
  delimit using symbols that can occur in the data (FLAG byte, e.g., 0x7E)
    Byte stuffing
      uses a special byte value (FLAG byte) to delimit frames
      sender prefixes any FLAG byte that appears in the payload field, with ESC byte
      sender also prefixes any ESC byte that appears in the payload field, with ESC byte
      Receiver strips all ESC bytes to get the data
      can resynchronize because 2 FLAG bytes in sequence indicates next frame

## Slide 8: Framing Example: PPP over SONET
Point to Point Protocol
  Data link layer protocol used to frame packets for transport over SONET
    SONET is the Physical Layer protocol used over ISP backbone fiber links
Protocol stacks

## Slide 9: Framing Example: PPP over SONET
Uses byte stuffing with an optimization
  Goal: eliminate ALL 0x7E (FLAG) occurrences in the payload data
    can then search the bit stream for 0111 1110 to identify frames
  Technique:
    At Sender:
      For a 0x7E (FLAG) in the data: replace it with 0x7D 0x5E instead i.e. 0x7D = ESC, 0x5E = 0x7E XOR 0x20
      For a 0x7D (ESC) in the data: replace it with 0x7D 0x5D instead
    At receiver:
      For a 0x7D in the data: drop it and XOR following byte with 0x20, to get the original (either 0x7D or 0x7E)

## Slide 10: Error Handling
Transmission errors are inevitable
  noise in the physical layer flips bits
    random thermal noise (isolated bit) or bursts of noise (block of bits)
  errors are the norm for wireless
  but: optical fiber are highly reliable - have tiny error rates

## Slide 11: Error Detection and Correction
Goal
  provide extra information so receiver can detect / correct errors
    adds redundant check bits to the actual data bits
    increases overhead bits on the channel
  BUT:
    add as few check bits as possible (adds to overhead)
    ensure low computation at sender and receiver
    not foolproof - check bits could be flipped just as easily as data bits!
      Physical layer treats all bits the same
  Strategy
    For highly reliable channels (fiber optics),
      cheaper to use error detection with retransmission
    For unreliable channels (wireless),
      cheaper to use error correction, since retransmission is just as likely to fail

## Slide 12: Error Detection
Motivating example
  Simply send two copies of the data: 010 010
  Evaluating its performance:
    how many errors will it correct? 0.
      if we receive 010 011, we don’t know which is correct.
    how many errors will it detect? perhaps 3
      if we receive 010 101, we can detect 3 errors.
    BUT: how many bit flips will cause it to fail? just 2!
      if we receive 011 011, just 2 bit flips cause our technique to give a wrong answer.
    And for this minimal protection, we used 50% of the link for overhead!
    Advanced codes use work done by mathematicians in Applied Mathematics

## Slide 13: Systematic Block Error Codes
  Sender
    receives bits from higher layer and generates a codeword (D+R bits)
      computes check bits as a function of a block of data bits (block code)
      appends these check bits (without modifications) to the data bits (systematic code)
    sends codeword (D+R) to the lower layer
  Receiver
    receives D+R bits with unknown errors
      recomputes check bits from the D bits
      error if does not match R’
      BUT: does not distinguish whether error is in data or checksum bits (R’)

## Slide 14: Error Correcting Codes
Goal:
  make ratio (correct : all ) codewords small
    random noise is unlikely to modify a codeword such that it maps to a different valid codeword – so easy to detect error
For D data bits, R check bits
  Ratio of (2D / 2D+R ) must be small (1/2R)  R must be large
  Randomly chosen codeword is unlikely to be correct
    with 16 check bits, there’s 1 in 65,535 chance of randomly picking a valid codeword

## Slide 15: Hamming Codes for error detection and correction
  Hamming distance of a code
    minimum number of bit flips required to change any valid codeword (D+R)1 into another (D+R)2
  Error Detection Rule: a code with distance d+1, can detect d errors.
  Error Correction Rule: a code with distance 2d+1, can correct d errors
  E.g.: code with 2 valid codewords: 111 for 1, 000 for 0
    Hamming distance: 3
    Can detect 2 errors
      sending 000, 2 bit flips results in: 001, 010, 011, 100, 101, 110
      receiver knows these are not valid codewords, so detects an error
    Can correct 1 error
      sending 000, 1 bit flip results in 001, 010, 100. Receiver corrects this to 000
      If more than 1 bit flip occurs, no correction is possible (010 could be 000 or 111)

## Slide 16: Hamming Distance
  4 valid codes
    D = 2, R=8, n = 10
    00 -> 00 000 00000, 01 -> 01 010 10101, etc.
  Hamming Distance: 5
    Detects: 4 bit errors
    Corrects: 2 bit errors

## Slide 17: Visualization of a Hamming code of distance 3
    brown are valid codewords, blue are invalid codewords
    For error detection:
      can detect 2 bit flip errors
      with 3 bit flips (hops) can go from one valid codeword to another
A
B
Valid
codeword
Error
codeword

## Slide 18: Visualization of a Hamming code of distance 3
  For correction:
    Box around A indicates codewords within a single bit flip error of A
    can correct single bit flips
    test received codeword to find its closest valid codeword
A
B
Valid
codeword
Error
codeword
Single
bit error
from A
Three bit
errors to
get to B

## Slide 19: Error Detection – Checksum
Sums data and uses n-check bits
  used by TCP, IP, and UDP
  16-bit one’s complement of the one’s complement sum of all 16-bit words
    one’s complement (negative of the number)
      invert the bits of a number; 001  110
    sum the data 16-bits at a time, and negate it
      Intuition: for the numbers 1, 5, and 7, the sum is 13, but the negated sum is -13 if we add 1, 5, 7, and -13, at the receiver, we should get 0.
    But: computers perform 2s complement arithmetic
      to do 1s complement addition on a computer that uses 2s complement arithmetic, track the bit that overflows to the carry field, and add it back to the low order bits

## Slide 20: Checksum
For the data: 84328634
  Step 1: arrange data in 16 bit words (put 0s in checksum position so we can use the same algorithm at the receiver), and add see: Binary subtraction and Hexadecimal addition 8432 8634 0000 ====== 10A66
  Step 2: Add the carry: 0A66 + 0001 = 0A67
  Negate to get negative sum: F598
  Send data as 84328634F598

## Slide 21: Checksum
At the receiver: 84328634F598
  Arrange data in 16 bit words 8432 8634 F598 ===== 1FFFE
  Add the carry: FFFE + 0001 = FFFF
  Negate to get: 0000 – no errors!

## Slide 22: Performance of Checksums
  Only error detection, not error correction
  Efficient and simple
  Detects burst errors of up to 16 bits
    sequence of errors in a row
    will affect only one 16 bit word, or two adjacent words in different places such that they can’t cancel out
  Max number of errors that we can detect is 1, two bits can fool it
  weak protection – it does not pick up:
    adding zeros
    swapping parts of the message
    complementary changes (add 16 in one place, and subtract 16 elsewhere)

## Slide 23: Cyclic Redundancy Checks
Take n bits of data, generate k check bits, such that n+k bits are evenly divisible by a generator C
  Intuition
    To send the number 302, with a 1 digit CRC, and generator C=3
    302x choose x such that the whole number is divisible by 3 3020 % 3 = 2 3021 % 3 = 0 I.e., our check digit should be 1
  CRCs do this with the math of Finite Fields
    Can’t work out this math from first principles (advanced math)
    binary sequences represent polynomials
    protection depends on the generator used

## Slide 24: CRC Computation
Sender algorithm
  extend n data bits with k zeros (based on degree of polynomial)
  divide by the generator polynomial C (based on terms of polynomial) E.g., x4 + x1 + 1
  use the remainder as the k check bits
    Division notes:
      done in modulo 2 arithmetic
        without carries in addition or borrows in subtraction
        i.e., add/subtract are same as XOR
      goes in by 1 if number of bits match
      goes in by 0 if number of bits are fewer
      see polynomial division

## Slide 25: CRC Computation
Receiver algorithm
  divide by the generator polynomial C and check for zero remainder
      ____________________
      1 0 0 1 1 | 1 1 0 1 0 1 1 1 1 1 0 0 1 0

## Slide 26: Cyclic Redundancy Checks
Industry standard 32-bit CRC (k=32) is 10000010 01100000 10001110 110110111
  detects odd number of errors, and bursts up to k bits
  used on Ethernet, Wifi, etc.
  Hamming distance is 4, can detect 3-bit errors
  stronger than checksum
    not vulnerable to systematic errors (adding 0s)
    detects moving of data
  Relies on polynomial division using XOR

## Slide 27: Error Detection in practice
CRCs are widely used on links
  Ethernet, 802.11, ADSL, cable
Checksum used in the Internet
  IP, TCP, UDP, ... but is weak

## Slide 28: Other Error Correction Codes
In practice, much more complex codes are used
  Convolutional codes
  Low density parity check (state of the art today)

## Slide 29: Data Link protocols – Reliability Strategies
  Error correction: Correct errors with an error correcting code
    handled using error correction codes or retransmissions
    used by lower layers (Physical and Link layers)
    goal is to improve performance (higher layers are oblivious of the errors)
  Error detection and recovery: detect errors and retransmit frame
    used by upper layers to address issues that cannot be corrected at the bit level
      unexpected message received on the other side
      cannot connect to the right receiving application on the other host

## Slide 30: Automatic Repeat reQuest (ARQ)
Simple auto resend mechanism
  used when errors are common (e.g., Wifi and TCP)
  Rules:
    receiver automatically ACKs correct frames
    sender automatically resends after a timeout, unless an ACK is received
  Normal case time sequence diagram
    Frame is received correctly and is ACKd
    ACK arrives before timeout expires
Frame
ACK
Timeout
Time
Sender
Receiver

## Slide 31: Automatic Repeat reQuest (ARQ)
  Loss and Retransmission case
    Data frame (or ACK frame) is lost inside a link
      frame arrives, but is corrupted, and receiver simply throws it away
      error is so severe that framing is affected – receiver does not detect start of frame, so it looks like the message is lost
    Sender does not receive ACK by timeout, so it resends the frame
  Considerations
    how long to set the timeout?
      if too big, link goes idle and wastes bandwidth
      if too small, sender resends early, wastes bandwidth
      For LAN, we can determine worst case E.g., for Wifi can work out max propagation delay
      For Internet as a whole, much harder
        a lot of variation in time (depends on host location)
        Pick reasonable value
Frame
Timeout
Time
Sender
Receiver
Frame
ACK
X

## Slide 32: Automatic Repeat reQuest (ARQ): Design Considerations
  Avoiding accepting duplicate frames as new frames (due to retransmissions)?
  Two scenarios:
    When an ACK is lost OR timeout is early
  Solution: All frames (data and ACKs) must carry sequence numbers
    Receiver checks sequence number to detect duplicates
Frame
ACK
X
Frame
ACK
Timeout
Sender
Receiver
New
Frame??
Frame
ACK
Frame
ACK
Timeout
Sender
Receiver
New
Frame??

## Slide 33: Stop and Wait protocol
Putting it all together
  Receiver ACKs every frame received
  Every frame carries a sequence number, to detect duplicates
    only 1 frame can be outstanding, so bit flag suffices as a sequence number
  Sender retransmits after a reasonable timeout, if no ACK received
  Sender sends next frame ONLY after previous is ACKed
  Normal case:
Frame 0
ACK 0
Timeout
Time
Sender
Receiver
Frame 1
ACK 1

## Slide 34: Stop and Wait protocol
With ACK loss
  Receiver knows it’s a resend
Frame 0
ACK 0
X
Frame 0
ACK 0
Timeout
Sender
Receiver
It’s a
Resend!

## Slide 35: Stop and Wait protocol
With early timeout
  Receiver knows it is a resend
  Sender gets 2 ACKs for Frame 0
    for the first ACK it does not know whether it was for the send or resend – but that does not matter
Frame 0
ACK 0
Frame 0
ACK 0
Timeout
Sender
Receiver
It’s a
Resend
OK …

## Slide 36: Stop and Wait protocol
Limitations
  allows only 1 frame to be outstanding from a sender at a time
  Okay for a LAN (used in Wifi)

## Slide 37: Stop and Wait protocol
  For Bandwidth B = 1Mbps, Delay D = 50ms
    RTT to send a frame and receive an ACK is 2D = 100ms
    Takes 100ms/frame: so in 1 second, we can send 10 frames
    if each frame is 10,000 bits, this is 100kbps ... on a 1Mbps link!
  For Bandwidth B = 10Mbps, Delay = 50ms
    we can still only send 10 frames per second!
      limited by the protocol and the RTT, not the bandwidth
    Max throughput is 100kbps, no matter how fast the link
  This is wasteful for networks with high bandwidth-delay product
    many packets could fit on the pipe
    sending just one is wasteful

## Slide 38: Sliding window protocol – window size
Problem: Stop and Wait uses a window of 1
To use the entire network bandwidth, B,
  we must send B bps for those RTT seconds (2D)
  I.e., send 2D * B = 100ms * 1Mbps = 100 * 10-3 sec * 106 bps = 100 * 103 bits = 100kb
    100kb will be stored at the receiver in the time it takes to send a frame and receive an ACK
  if frame is 10Kb, then W=10 frames
  IF we increase B to 10Mbps, W = 100 frames
    sliding window gets larger with higher capacity links
1
2
3
4
5
6
7
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 39: Sliding Window Protocol
Many variations
  depending on how buffers, ACKs, and retransmissions are handled
  Go Back N
    simple, but inefficient
    works well when errors are rare, but if line is poor, wastes a lot of bandwidth on retransmitted frames
    requires less receiver buffer space (only 1 buffer)
  Selective Repeat
    more complex, better performance
    requires more buffer space (usually, set to W)

## Slide 40: Go-back-n Protocol - Errors
  Send window size = 7. Receive window size = 1.
    Receiver discards all out-of-order frames, sending no ACKs for them
    Eventually sender times out, and retransmits all unACKed frames, in order starting with the lost/damaged one
    Can waste a lot of bandwidth if the error rate is high

## Slide 41: Selective Repeat Protocol - Errors
  Send window size = 4, Receive window size = 4.
    Bad frame received is discarded
    But any good frames received after it, are accepted and buffered
    When sender times out, only the oldest unACKed frame is retransmitted
    if that frame arrives correctly, receiver can deliver all the buffered frames to the network layer, in sequence order
    can be combined with a NAK for frame errors, to cause retransmits before the timer expires. If NAK is lost, timeout causes retransmit.

## Slide 42: Sliding Window - Sender
Sender
  buffers up to W frames (the sliding window size) until they are ACKed
    buffering allows it to resend them if needed
  Markers delineate three categories of frames
    LFS = Last Frame Sent (highest number frame sent, but not yet ACKd)
    LAR = Last ACK Received (highest in-sequence ACK that has been received)
    Sliding window allows us to have a difference between LFS and LAR – up to W frames can be sent into the network, without being ACKed.

## Slide 43: Sliding Window - Sender
Sender
  Categories
    ACKed
      All frames up to LAR have been sent, ACKd, and we’ve received the ACK
    UnACKed
      All frames between LFS and LAR have been sent, but ACKs not yet received
    Unavailable frames:
      frames that we can’t send yet, because our window is not big enough

## Slide 44: Sliding Window - Sender
Sender
  can keep sending while LFS – LAR <= W (here, we can send 1 more frame)
  Sliding window moves as we send packets and receive ACKs

## Slide 45: Sliding Window - Sender
Case 1: new frame is accepted for sending
  Frame can be sent right away, since since LFS – LAR < W
    we only had 4 frames outstanding, and our W was 5
  LFS is updated
  LAR is not updated since we have not received any ACKs
  At this point, LFS-LAR=W,
    no more frames can be sent until some of the Unacked frames are ACKed

## Slide 46: Sliding Window - Sender
Case 2: next higher ACK arrives from the receiver
  increment LAR
  we now have only 4 frames outstanding in the network
  window is still 5, but it has now slid over to the right
    opens up space for 1 new segment to be sent into the network
  LFS – LAR  4 (can send one more, since W=5)

## Slide 47: Sliding Window – Go-back-N
Receiver has only 1 buffer - for the next frame
  State variable, LAS = LAST ACK SENT
On receive
  if sequence number is LAS+1, accept and pass to network layer; update LAS; and send ACK
  Otherwise discard (it was received out of order)
    sender will notice this (at timeout) and retransmit

## Slide 48: Sliding Window – Go-Back-N sender
  Retransmissions
    uses a single timer to detect losses
    if frame is not ACKed within a timeout,
      assumes it is lost, and that receiver has thrown away all frames after it
      resends all buffered packets in the current window, starting at LAR+1
  Sequence Numbers
    need W+1 (only one ACK outstanding at a time)
    Implement with an N-bit counter that wraps around at 2N – 1.
    e.g., N=8: ..., 253, 254, 255, 0, 1, 2, 3, ...

## Slide 49: Bidirectional Go-Back-N
Additional Concepts
  Cumulative ACK
    When an ACK comes in for frame n, all prior frames (n-1, n-2, etc.) are considered automatically ACKed
  Piggybacking ACKs
    receiver does not ACK a frame on arrival
    receiver waits until it has a packet to send and attaches ACK to the outgoing frame
      ACK gets a free ride on the header of the next outgoing data frame
      much cheaper than sending a separate frame (complete with header and checksum)
    receiver must have enough traffic to send
      Else, traffic will grind to a halt once the sender’s send window is hit
    Option is to set a timeout – if no outgoing packet is ready by timeout, ACK is sent by itself

## Slide 50: Protocol 5

## Slide 51: Protocol 5

## Slide 52: Protocol 5

## Slide 53: Protocol 5

## Slide 54: Protocol 5

## Slide 55: Protocol 5

## Slide 56: Optional Section
  The remaining slides are retained for optional additional reading
  You will not be tested on these
Optional

## Slide 57: Constructing Hamming codewords (to correct single bit errors)
Determining the number of check bits R for data bits D to correct single bit errors:
  D <= 2R – R – 1 (OR) R <= 2R – 1 – D
  for D=4, we get R=3, for a 7 bit codeword
    Calculate R <= 2R – 5 R=1, gives us 1 <= -3 (no!) R=2, gives us 2 <= -1 (no!) R = 3, gives us 3 <= 3 (yes!)
Optional

## Slide 58: Constructing Hamming codewords for error correction
Optional
Example: data = 0101, 3 check bits
  write out the 7 bits, numbered from left to right
  bits at positions of powers of 2 are check bits, rest are data bits
  check bit for position p is a parity sum over all positions that have the p term in their binary values
    check bit at position 1, covers bit positions 1, 3, 5, 7: p1 = 0 + 1 + 1 = 0
    check bit at position 2, covers bit positions 2, 3, 6, 7: p2 = 0 + 0 + 1 = 1
    check bit at position 4, covers bit positions 4, 5, 6, 7: p4 = 1 + 0 + 1 = 0
_ _ _ _ _ _ _
1 2 3 4 5 6 7
_ _ 0 _ 1 0 1
1 2 3 4 5 6 7
0 1 0 0 1 0 1
1 2 3 4 5 6 7

## Slide 59: Error correction at the Receiver
Optional
  Recompute all check bits using the check bit parity itself
    p1 covers positions 1, 3, 5, 7: p1 = 0 + 0 + 1 + 1 = 0
    p2 covers positions 2, 3, 6, 7: p2 = 1 + 0 + 0 + 1 = 0
    p4 covers positions 4, 5, 6, 7: p3 = 0 + 1 + 0 + 1 = 0
    If all parity bits are 0, then extract data as 0101
  If there is an error,
    parity bits compute as: p1 = 0 + 0 + 1 + 1 = 0, p2 = 1 + 0 + 1 + 1 = 1, p4 = 0 + 1 + 1 + 1 = 1.
    Arrange parity bits as: 011 and flip the bit at that position (6) to get the data
0 1 0 0 1 0 1
1 2 3 4 5 6 7
0 1 0 0 1 1 1
1 2 3 4 5 6 7

## Slide 60: Sliding Window – Selective Repeat
  Receiver does more work, but can use network more efficiently
  Receiver passes data to upper layer in sequence order
  BUT: instead of 1 buffer, has W buffers (size of sender’s sliding window)
    Goal is to reduce retransmissions
    it will accept frames out of order, and will hold on to them
    when it later gets the frame that was missing, it sends all queued frames in sequence order up to the network layer.
  Process
    when a frame is received
      if it falls within the window (from LAS+1 to LAS+W), store it in corresponding buffer
      check buffer if any frames starting from LAS+1 have arrived in order
        if they have, pass those in-order frames up to the Network layer
        update LAS to the highest frame which has been delivered to the network layer
        send an ACK
          with the current LAS if it has moved OR
          with resend ACK with old LAS (tells sender that frames up to and including this one have been received. Gives sender an idea of which packets may have been lost.)
Optional

## Slide 61: Sliding Window – Selective Repeat
  Retransmissions
    uses a timer per unaACKed packet
    if it times out, just that frame is retransmitted
    hope is to avoid having to resend a whole window’s worth of frames
      can do this because receiver is also buffering packets that arrive out of order
  Sequence numbers
    need W numbers for packets, and W for ACKs of earlier packets
    2W sequence numbers
Optional