## Slide 1: ICS 460 – Medium Access Control Sublayer
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Introduction
Types of networks – by technology type
  Point to Point channels
    mainly used in WANs
  Broadcast channels (or multi-access channels)
    mainly used in LANs
    key issue is to allocate a single channel among competing users
      channel connects each user to other users
      any user who uses the channel interferes with others who also wish to use it
      portion of the wireless spectrum in a region, or single wire to which nodes are connected

## Slide 3: Goals
Simple model to explore how nodes share a single link
  e.g., multiple laptops want to send to a single WiFi access point
  simplified mode: multiple hosts attached to a single wire
Assume no-one is in charge; this is a distributed system
  all nodes have a local view, i.e., can communicate with other nodes
  but have no global view of the topology
  no one is in charge of what is going on in the network
MAC sublayer focus
  determine who gets access to a channel

## Slide 4: Statistical multiplexing
Multiplexing technique
  dynamic channel allocation
    host claims access to the shared channel
    avoids/detects collisions and resends if required
    uses randomization to handle multiple access
    preferred for computer data traffic

## Slide 5: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Classic Ethernet
  nodes share 10Mbps coax cable with baseband signals
  Listening for activity before sending
  easy to do with wires (not wireless)
  but does not eliminate collisions
    possible to hear nothing even when another is sending, because of delay
    Reduces cost of collisions by detecting them and aborting transmission
      hardware listens to channel while transmitting. If signal read back is different from what it is sending, it indicates a collision
X
X X X X X X X X
Jam!
Jam!

## Slide 6: Ethernet Frame Format
  Addresses identify sender and receiver
  CRC-32 for error detection
  no ACKs or retransmission
  Start of frame identified with physical layer preamble
Packet from Network layer (IP)

## Slide 7: Modern (Switched) Ethernet
Based on switch to connect nodes - NOT multiple access
  Hosts are wired to a switch with twisted pair wires
  Switch connects pairs of hosts
  All ports are wired together;
    more convenient to run wires to one location
    more reliable than shared wire
      easy to diagnose broken wires
  Better scalability than using a hub
    E.g., 100 Mbps per port, instead of 100Mbps shared across all nodes on a cable or hub
Switch
Switch
Twisted pair
Switch ports

## Slide 8: How do switches work?
  Forwarding
    use frame address to connect input port to right output port – do NOT look at IP address
    let hosts be moved around readily
    multiple frames may be switched in parallel
    port may be used for both input and output (full duplex)
      Acts as point-to-point link, so no multiple access protocol needed
  Uses the Backward Learning algorithm
    to fill the forwarding table: looks at the source address of input frames
    to forward: sends to a known port; or broadcasts to all ports
. . .
1
2
3
4
1  4
and
2  3

## Slide 9: Backward Learning algorithm
  0. Start off with no knowledge of topology; and empty table
  1. A sends to D We know A’s port. But we don’t know D’s: broadcast over all other ports (2, 3, 4)
  2. D sends to A we know both A’s and D’s connected ports - forward to port 1.
  3. A sends to D we know D’s port, so forward to port 4.
  Switch continues learning the address of other hosts.
Switch
D

## Slide 10: Problem: Forwarding Loops
  Loops may occur!
    intentionally: redundancy for failures
    unintentionally: simple mistake
  A  F in a topology with loops
    A C, C broadcasts on B, D-Left, D-Right
    D-Left  D, D broadcasts on C-Right, E, F
    D-Right  D, D broadcasts on C-Left, E, F
    C-Right  C, C broadcasts on D-Left, A, B
    C-Left  C, C broadcasts on D-Right, A, B
    D-Left  ...
    D-Right  ...
    and so on
Left / Right
A
B
C
D
E
F

## Slide 11: Solution: Spanning Tree Algorithm
  Switches find a spanning tree for the topology - collectively
    Spanning tree: subset of links that is a tree (no loops) and reaches all switches
    switches forward as normal on the spanning tree
    broadcasts will go up to the root of the tree, and down all the branches
Topology
One ST
Another ST
Root

## Slide 12: Spanning Tree algorithm
Characteristics
  Distributed, non centralized:
    all switches run the same algorithm
    they start with no information
    operate in parallel and send messages
    always search for the best solution
  Ensures a highly robust solution
    works for any topology, with no configuration
    adapts to link/switch failures

## Slide 13: Spanning Tree Algorithm
  Outline
    elect a root node of the tree (switch with the lowest address)
      each switch initially believes it is the root of the tree
    grow tree as shortest distances from the root (lowest address breaks ties)
      each switch sends periodic updates to neighbors with:
        its address, address of the root, and distance (in hops) to root
      switches favor ports with shorter distances to lowest root
        uses lowest address as a tie break for distances
    turn off ports for forwarding if they aren’t on the spanning tree
C
Hi, I’m C, the root is A, it’s 2 hops away
or (C, A, 2)

## Slide 14: Spanning Tree Example
  1st round, sending:
    A sends (A, A, 0) to say it is root
    B, C, D, E, and F do likewise
  1st round, receiving:
    A still thinks it is (A, A, 0)
      its switch address is lower than C’s or E’s.
    B still thinks it is (B, B, 0) ... likewise for C and F
    C updates to (C, A, 1)
      C receives (A,A,0) and (B,B,0)
      uses lowest switch address to break tie
    D updates to (D, C, 1)
      D receives (C,C,0), (E,E,0), and (F,F,0)
    E updates to (E, A, 1) ... lower of A and D
    F updates to (F, B, 1) ... lower of B and D
A,A,0
B,B,0
C,A,1
D,C,1
E,A,1
F,B,1
A,A,0
B,B,0
C,C,0
D,D,0
E,E,0
F,F,0

## Slide 15: Spanning Tree Example
  2nd round, sending:
    Nodes send their updated state
  2nd round, receiving:
    A remains (A, A, 0)
    B updates to (B, A, 2) via C
      receives (C,A,1) and defers to lower root address
    C remains (C, A, 1)
    D updates to (D, A, 2) via C-Left (picking one port)
    E remains (E, A, 1)
    F remains (F, B, 1)
A,A,0
B,A,2
C,A,1
D,A,2
E,A,1
F,B,1
A,A,0
B,B,0
C,A,1
D,C,1
E,A,1
F,B,1

## Slide 16: Spanning Tree Example
  3rd round, sending:
    Nodes send their updated state
  3rd round, receiving:
    A remains (A, A, 0)
    B remains (B, A, 2) via C
    C remains (C, A, 1)
    D remains (D, A, 2) via C-Left
    E remains (E, A, 1)
    F updates to (F, A, 3) via B
A,A,0
B,A,2
C,A,1
D,A,2
E,A,1
F,A,3
A,A,0
B,A,2
C,A,1
D,A,2
E,A,1
F,B,1

## Slide 17: Spanning Tree Example
  4th round, sending:
    steady state has been reached
    Nodes turn off forwarding on some ports
      eliminate duplicate paths
      pick lowest switch address as tie breaker
  Algorithm continues to run
    adapts by timing out information
    e.g., if A fails, other nodes forget it, and B will become the new root
A,A,0
B,A,2
C,A,1
D,A,2
E,A,1
F,A,3

## Slide 18: Spanning Tree Example
  Forwarding proceeds as usual on the ST
    Black arrows - spanning tree
    Pink arrows – broadcast from D looking for F
    Green arrows – route from F to D
  D  F (broadcast since we don’t know its port)
    D C-Left
    C  A, B
    A  E
    B  F
  F  D (we know where D lives)
    F  B
    B  C
    C  D
    (not the best route, F is directly connected to D!)
A,A,0
B,A,2
C,A,1
D,A,2
E,A,1
F,A,3

## Slide 19: WiFi or 802.11
  started in the 90s
  clients get connectivity from a wired Access Point (AP)
  multi access problem for shared channel
  Uses 20/40MHz channels on ISM bands
    802.11b/g/n on 2.4GHz
    802.11a/n on 5GHz
Access Point
Client
To Network

## Slide 20: Wireless Channel
Wireless
  Does not fit into CSMA/CD model
    Nodes may have different areas of coverage – does not fit Carrier Sense
    Nodes can’t hear while sending – can’t Collision Detect
      Inability to do CD results in wastage for wireless (cannot abort in middle of send)
  signal is broadcast, and received where there is sufficient SNR

## Slide 21: Hidden and Exposed Terminals
Hidden terminals
  Nodes A and C are hidden when sending to B
  Can’t hear each other (to coordinate), yet collide at B
  would prefer to avoid collisions (inefficient)
Exposed terminals
  B and C are exposed terminals when sending to A and D
  can hear each other, yet don’t collide at receivers A and D
  would prefer to concurrently send to increase performance

## Slide 22: 802.11 uses CSMA/CA for Multiple Access
    both B and C need to send
    Carrier Sense: they sense medium is busy, so they wait until it is free
    Collision Avoidance: B and C pick a random backoff time to wait
    C picks a smaller gap and goes first.
    B suspends its backoff until after C is done, and then transmits its frame
Time
Send?
Send?

## Slide 23: 802.11 Link Layer
  Multiple access uses CSMA/CA; RTS/CTS optional
  Frames are ACKed and retransmitted with ARQ
  Needs 3 addresses (due to AP)
  Error detection uses 32-bit CRC
Packet from Network layer (IP)

## Slide 24: ALOHA Network
Seminal computer network
  connected the Hawaiian islands in the late 60s
  Simple idea
    node just sends when it has traffic
    if there is a collision (no ACK received) then wait a random time, and resend
    some frames will be lost, but many will get through
Additional

## Slide 25: ALOHA Protocol
Result
  simple decentralized (no SPoF) protocol that works well under low load
  Not efficient under high load
    at most 18% efficiency
    improvement: divide time into slots, and efficiency goes up to 36%
Additional

## Slide 26: Classic Ethernet (IEEE 802.3)
Inspired by ALOHA, invented in 1973 for LANs
  nodes share 10Mbps coax cable with baseband signals
  Multiple access with “1-persistent CSMA/CD with BEB”
  hugely popular in 80s and 90s
Additional

## Slide 27: CSMA/CD Complications
Want everyone who collides to know that it happened
  time window in which a node may hear of a collision is 2D seconds
  Impose a minimum frame length - that lasts for 2D seconds
    so node can’t finish before collision
    Ethernet uses a minimum frame length of 64 bytes
X
X
Additional

## Slide 28: CSMA Persistence
What should a node do if another node is sending
Idea: wait until it is done, and send
Problem
  multiple waiting nodes will queue up then collide (likelihood increases with increased load)
What now?
Now!
Now!
Uh oh
Additional

## Slide 29: CSMA Persistence
Better solution
  if there are N queued senders, we want each to send with probability 1/N
Binary exponential Backoff (BEB)
  estimates probability
    1st collision, wait 0 or 1 frame times
    2nd collision, wait 0 to 3 frame times
    3rd collision, wait 0 to 7 frame times
  BEB doubles interval for each successive collision
    quickly gets large enough to work
    very efficient in practice
Send p=½
Whew
Send p=½
Additional

## Slide 30: Nodes can’t hear while sending
CD lowers costs with wires
  detecting collisions while sending, and aborting
  Inability to do CD results in wastage for wireless
Additional

## Slide 31: Possible solution – Multiple Access Collision Avoidance
MACA uses a short handshake instead of CSMA
  refinement of MACA is used by 802.11
Protocol rules
  sender node transmits a Request to Send (RTS) with a frame length
  receiver replies with a Clear to Send (CTS) with a frame length
  sender transmits the frame while nodes hearing the CTS stay silent
    collisions on the RTS/CTS are still possible, but less likely (short bursts)
Additional

## Slide 32: Solving the Hidden terminal problem with MACA
AB with hidden terminal C
  A sends RTS to B
  B sends CTS to A, and C gets it too
  A sends frame while C defers
D
C
B
A
RTS
D
C
B
A
RTS
CTS
CTS
Alert!
Frame
Quiet...
Additional

## Slide 33: Solving the Exposed terminal problem with MACA
BA, and CD simultaneously
  B and C send RTS to A and D
  A and D send CTS to B and C
  B and C send frames to A and D
D
C
B
A
RTS
RTS
D
C
B
A
RTS
RTS
CTS
CTS
All OK
All OK
D
C
B
A
Frame
Frame
Additional

## Slide 34: Switch internals - buffers
Buffers for multiple inputs to send to one output
  sustained overload will overflow buffer, and lead to frame loss
. . .
. . .
. . .
. . .
Input Buffer
Output Buffer
Fabric
Input
Output
XXX
Loss!
Additional

## Slide 35: Learning with Multiple Switches
  Assuming no loops, Backward learning also works with multiple switches
  E.g., A sends to D
    B1 marks A’s port (1); and broadcasts out to ports 2, 3, and 4
    B2 marks A’s port (4) and broadcasts out to ports 1, 2, 3
      H1 is a simple hub, so frames are available to all its hosts
      frame arrives at port 1 for D
  D sends to A
    B2 marks D’s port (1) and sends out on A’s port (4)
    B1 marks D’s port (4) and sends out on A’s port (1)
Switch
Additional