## Slide 1: ICS 460 – Network Layer
Damodar Chetty
Physical
Link
Network
Transport
Application

## Slide 2: Introduction
Where we are
  We can build networks with links and switches, and send frames between hosts
  But:
    switches don’t scale to large networks
      tables must have entries for all destinations in the world
      broadcasting to new destinations would send packets to the whole internetwork!
    switches don’t work across more than one link layer technology
      Hosts on Ethernet, 802.11, 4G, ...
    spanning trees are not efficient for routing - does not pick shortest paths
      wastes bandwidth - the most scarce network resource.

## Slide 3: Network Layer
Fixes shortcomings in Switches
  Scaling
    Provides an addressing hierarchy, in the form of prefixes (focus of this lecture)
  Heterogeneity (Supports different link layer technologies)
    IP for internetworking (the narrow waist of the Internet)
  Uses link bandwidth well
    lowest-cost routing
    Quality of Service

## Slide 4: Key Terms
Routing
  process of computing all of the paths through the network, so that you will be prepared to forward packets when they arrive
  it is a network-wide process, and is expensive
Forwarding
  process of handling a packet when it arrives, and sending it on its way
  uses the routing table generated by the routing algorithm
  it is a local node process, and is fast

## Slide 5: Store and forward Packet Switching
  Host H1 transmits a packet to its nearest router
    on own LAN or over a point-to-point link to the ISP
  Router will
    Buffer packet until fully received (stores it temporarily)
    Verify its checksum
    Forward it to the next router along the path to its destination host.
    not stored for very long – except if there is contention for the destination port.
ISP’s equipment

## Slide 6: Network Service Models - Datagrams
  Post Office model: Each packet contains a destination address
    each router uses it to forward each packet; possibly on different paths
  Each router has a forwarding table keyed by destination IP network prefix
    gives next hop for each destination
    can change due to congestion, failure, …
      A learns of congestion along A-C-E
      updates its routing table to send #4 to B instead
A’s table (initial) A’s table (later) C’s Table E’s Table
ISP’s equipment

## Slide 7: Network Service Models - Datagrams
  Post Office model: Each packet contains a destination address
    each router uses it to forward each packet; possibly on different paths
  Each router has a forwarding table keyed by destination IP network prefix
    gives next hop for each destination
    can change due to congestion, failure, …
      A learns of congestion along A-C-E
      updates its routing table to send #4 to B instead
  Dominant model on the Internet
ISP’s equipment

## Slide 8: Network Service Models - Virtual Circuits
    path from source to destination router is first established - a virtual circuit (VC)
      stored in all routers along that path, and used to forward all packets for a given VC
      routing decisions made only on new VC setup and remains in force for entire session
    Packet identifies a VC using a locally unique (to the router) label
    VC #1 is the connection between H1 and H2 via A->C->E
    VC #2 is the connection between H3 and H2
      Locally to H3, the label is 1, but A uses label switching to change it to 2 to keep it unique at C
    ISPs use MultiProtocol Label Switching (MPLS) to setup long paths through their network

## Slide 9: Datagrams vs Virtual Circuits
Complementary strengths

## Slide 10: Internetworking
  Combining different networks into a larger network
    Different networking technologies exist (Ethernet, 802.11, etc.)
      Lots of differences between these technologies: e.g.,
        Service models (datagrams, Virtual Circuits)
        Packet sizes (how to pass an 8000-byte packet through a network whose max size is 1500 bytes?)
        Addressing (flat or hierarchical?)
        QoS (how to guarantee QoS when one network provides QoS, and the other only best effort service?)
    Internetworking hides the differences with a common protocol
      IP is the narrow waist of the Internet that defines a universal packet format
        that all routers recognize (network interconnection device, works at network layer)
        that can pass through any network
      many different link technologies below, many applications above
      BUT:
        lowest common denominator service
        e.g., does not preserve QoS
      Applications implement any higher level services needed
7. Application
4. Transport
3. Internet
2/1. Link
Ethernet
802.11
IP
TCP
UDP
HTTP
SMTP
RTP
DNS
3G
DSL
Cable

## Slide 11: Internet Protocol (IP)
  Network layer of the Internet
    Common format to represent packets
      bits are transmitted from left to right and top to bottom
    Two main sections: Header and Payload
    Provides a layer of addressing above link addresses
      IPv4 carries 32 bit source and destination interface addresses on each packet
      Globally unique
    Options are rarely used
Payload (e.g., TCP segment)

## Slide 12: IPv4
    Version of the protocol (e.g., 4)
    Internet Header Length: length of the header up to the start of the payload
    Total length: header + payload (max of 64KB)
    TTL: limits packet lifetimes, decremented on each hop, and discarded when 0
    Protocol: which transport layer (TCP or UDP) to give the assembled packet to
    Header checksum
      recomputed at each hop because at least one field always changes (TTL)
Payload (e.g., TCP segment)

## Slide 13: IPv4
Handle fragmentation and packet size differences
  Id: all fragments of a packet contain the same id
  DF: don’t fragment – used to discover the path’s Max Transmission Unit
  MF: More fragments – set to 1 for all fragments except the last.
  Fragment Offset: ordering of fragment within a packet
Payload (e.g., TCP segment)

## Slide 14: IPv4 Addresses
  Internet Assigned Numbers Authority (IANA) owns all public IP addresses
    Internet Corporation for Assigned Names and Numbers (ICANN)
      Created to manage network numbers since the late 1990s
    Delegates address space to Regional Internet Registries (RIRs)
    RIRs dole out blocks of addresses
    Companies (e.g., ISPs) apply to these bodies for IP addresses.
      ISPs redistribute to end-user organizations or to smaller ISPs
    Companies assign these addresses to computers on their network (using DHCP)
  IP address assignment is an ongoing process as companies grow.
https://www.icann.org/en/system/files/files/functions-basics-07apr14-en.pdf

## Slide 15: IPv4 Addresses
  IPv4 uses 32-bit addresses
    Written in dotted-quad notation: four 8-bit numbers separated by dots
    Address is hierarchical: comprised of a network prefix (address) and a host address
    IP addresses are allocated in blocks called IP prefixes, e.g., 18.13.0.0/16
      hosts on one network are all in the same prefix
      high order bits (the network id) are common across all hosts in a network
      Written in “IP address/length” notation
        The 128.13.0.0/16 prefix has host addresses from 128.13.0.0 to 128.13.255.255
        An L-bit prefix, has the first L bits fixed, and contains 232-L host addresses
aaaaaaaabbbbbbbbccccccccdddddddd ↔ A.B.C.D
8 bits
8 bits
8 bits
8 bits
00010010000111110000000000000001 ↔
18.31.0.1

## Slide 16: IPv4 Addresses – IP Prefixes
  Characteristics
    More specific prefix: longer prefix, fewer IP addresses
    Less specific prefix: shorter prefix, more IP addresses
000100100001111100000000xxxxxxxx ↔
128.13.0.0/16
Prefix
length
Addresses
in prefix
/8
/16
/24
/32
/0
20
28
216
224
232
Less specific
More specific
18.31.0.0/24
1000000000001101xxxxxxxxxxxxxxxx ↔

## Slide 17: IP Prefixes
  Benefit: Prefixes let Internet routing scale
      routers forward packets based on ONLY the network portion of a host’s address
        Routers do not consider the host portion while forwarding - all packets for all hosts on the same network are sent in the same direction
        host portion is only relevant once the packet arrives at its destination network
      Despite over a billion hosts, routing tables need to track much fewer prefixes (0.3 to 1 M)

## Slide 18: Subnets and Aggregation
  We can go even farther for scaling to reduce the entries needed in a routing table
    split a prefix (subnets) and join prefixes (aggregation)
      Subnets: internally split one less specific prefix into multiple more specific prefixes
        to the outside world, the less specific prefix acts as a single network
        but internally we split it into more specific prefixes – called subnets
      Aggregation: externally join multiple more-specific prefixes into one larger less-specific prefix
        represents multiple networks as a single larger network
        can be done if all of the addresses are in the same portion of the address space
        used by routers in the middle of the Internet
I’m the whole region
Region
1
2
3
IP /16
IP1 /18
IP2 /18
IP3 /18
I’m the whole region
Region
1
2
3
IP /16
IP1 /18
IP2 /20
IP3 /22

## Slide 19: Subnets
  Company leases one IP prefix, and splits it up into multiple internal sub networks
    routers on the Rest of the Internet do not know about internal subnets
      they send all traffic for this prefix to the company’s edge router
    Company’s edge routers know the subnet masks for all internal networks
      incoming packets are forwarded to the matching subnet
      outgoing packets are simply sent on the line to the ISP
64K addresses
One prefix sent to rest of Internet
16K
32K
8K
University
Rest of Internet

## Slide 20: Subnets
  When a packet arrives at the edge router, it forwards it on to the right subnet
    Its routing table only needs the prefix for each subnet
    ANDs destination IP address with each subnet mask to determine destination subnet
      Incoming packet has destination address: 128.208.2.151
      Compare against CS subnet:
      Compare against EE subnet:

## Slide 21: Aggregation
  Company’s edge routers send
    outbound traffic out the line that connects to the rest of the Internet
    Inbound traffic to the appropriate subnet (needs an entry per subnet)
  Routers in the middle of the Internet
    have no easy default – need entry for each prefix on the Internet (1m+ networks)
    to reduce the prefixes they must know about, they build supernets
      join prefixes for several networks into a single larger, less-specific, prefix
        works only if the prefixes fall within the same portion of the address space
      networks do not belong to the same entity
    reduces router tables to around 200,000 prefixes

## Slide 22: Aggregation
  An ISP has the following block of addresses
    [194.24.0.0 to 194.24.11.25] and [194.24.16.0 to 194.24.31.255]
    it does not own [194.24.12.0 to 194.24.15.255] within this range
    it claims to own the complete range [194.24.0.0 to 194.24.31.255] to NY router
  NY router sends traffic in this full range to this ISP router
  PROBLEM: Packets addressed to host 194.24.12.1 should be sent elsewhere!
    Longest Matching Prefix rule addresses this issue
One prefix sent to rest of Internet
\
ISP
Rest of Internet

## Slide 23: Forwarding Packets
  IP Forwarding uses a table that lists the next hop, by IP prefix
  Longest Matching Prefix forwarding rule
    Prefixes in the table can overlap due to aggregation (supernets)
    for each packet, find the longest prefix that contains the destination address (most specific entry)
    Forward the packet to the next hop router for that prefix
192.24.0.0
192.24.63.255
/18
/22
192.24.12.0
192.24.15.255
IP address
192.24.6.0  D
192.24.14.32  B
192.24.54.0  D
More
specific
D
B
D

## Slide 24: Getting IP addresses
Problem
  Node waking up for the first time needs its IP address, IP address of its router, network prefix, DNS server, time server, etc.
  Its Ethernet address is hardwired into its NIC
Options
  Manual configuration – but is tedious and error-prone esp. for large networks
  Dynamic Host Configuration Protocol (since 1993)
    automatically configures addresses and other parameters
Use A.B.C.D
What’s my IP?

## Slide 25: Address Resolution Protocol – sending an IP packet
Problem
  node needs link layer addresses to send a frame over the local link
  How to transform a destination IP address into a link address?
ARP
  node broadcasts the IP to all nodes, asking node with that IP to identify itself
  node maps local IP addresses to the corresponding Link layer addresses
Source
Ethernet
Dest.
Ethernet
Source IP
Dest.
IP
Payload …
Link layer
From
DHCP
From
NIC
From ARP

## Slide 26: IP errors – Internet Control Message Protocol
ICMP
  sits on top of IP (sets Protocol = 1 in IP packet header)
Provides error reporting and testing (e.g., Ping)
  when router encounters an error while forwarding
    it sends an ICMP error report back to the IP source address
    it discards the problem packet; host needs to rectify
  Ping relies on a Echo Request, which requires an immediate Reply
Report then toss it!
Oh, now I see …
XXXXXXX
ICMP report

## Slide 27: traceroute
repurposes TTL and ICMP functionality
  TTL field is decremented every router hop, with ICMP error if it hits 0
    protects against forwarding loops
  sends probe packets, increasing TTL starting from 1
  ICMP errors identify the routers on the path
. . .
Local
Host
Remote
Host
1 hop
2 hops
3 hops
N-1 hops
N hops

## Slide 28: Public/Private IP addresses
Public IP address. e.g., 18.31.0.1
  Valid destination on the global Internet
  Must be allocated before use (by IANA and regional bodies)
  Mostly exhausted
Private IP addresses
  can be used freely within private networks
  10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
  Need public IP address(es) and NAT to connect to the global Internet

## Slide 29: Network Address Translation
connects an internal network to an external network
  motivated by IP address scarcity
  commonly used in home networks, built into wireless router
  converts private IP addresses (many) to one public IP address
ISP
Unmodified computers at home
Looks like one
computer outside
NAT box

## Slide 30: How NAT works
Keeps an internal/external address table
  uses IP address + TCP port
  so really is address and port translation
Need ports to make mapping 1:1 since there are fewer external IPs
What ISP thinks
What host thinks

## Slide 31: How NAT works
Internal  External
  Look up and rewrite source IP/port
External  Internal
  Look up and rewrite Destination IP / port
NAT box
External
destination
Internal
source

## Slide 32: IPv6
Internet is growing
  over 1 billion hosts, and we’re still using 32-bit addresses
  now assigning addresses from leftover blocks held by the regional registries
IPv6
  effort started by the IETF in 1994; standard in 1998
  much larger addresses, 128 bits
    new notation: 8 groups of 4 hex digits (16 bits)
    omit leading zeros, groups of zeros e.g., 2001:0db8:0000:0000:0000:ff00:0042:8329
  Other improvements
    streamlined header processing
    flow label to group packets
    better fit with advanced features (mobility, multicast, security)

## Slide 33: IPv6 Transition
Problem: How to deploy IPv6
  IPv4 is incompatible with IPv4
Tunneling (carry IPv6 over IPv4)
  Native IPv6 islands connected via IPv4
  Tunnel acts as a single link across IPv4 network
    carries IPv6 packets across IPv4 network
Optional

## Slide 34: Tunneling
Difficulty:
  must set up tunnel endpoints and routing
IPv6
Link
User
User
IPv4
Link
IPv6
IPv6
Link
IPv6
Link
IPv4
Link
IPv6
IPv6
Link
Native IPv4
Native IPv6
Native IPv6
Tunnel
Optional

## Slide 35: Host/Router distinction
  Hosts can reach other hosts on their own prefix (own network)
  But they send remote traffic (outside the prefix) to their nearest router
  Routers do the routing – know the way to all destinations
  Forwarding table for a host on the network
    relies on the longest matching prefix algorithm
    0.0.0.0/0 is a default route that catches all IP addresses
It’s my job to know which way to go …
Not for my network? Send it to the router
Optional