## Slide 1: Network layer: “control plane” roadmap
routing protocols
  link state
  distance vector
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 2: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 3: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time

## Slide 4: Network layer: “control plane” roadmap
routing protocols
  link state
  distance vector
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 5: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 6: Dijkstra’s link-state routing algorithm
centralized: network topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
notation

## Slide 7: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 8: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
4,y
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
4,y
3,y
5,u
∞
∞
1,u
2,u
∞
2,x
4,x
2,u
4,y
3,y
2,u
uxyvwz
uxyvw
uxyv
uxy
ux
u
v
w
x
y
z
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a

## Slide 9: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 10: Dijkstra’s algorithm: discussion
algorithm complexity: n nodes
each of n iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2) complexity
more efficient implementations possible: O(nlogn)
message complexity:
each router must broadcast its link state information to other n routers
efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 11: Network layer: “control plane” roadmap
routing protocols
  link state
  distance vector
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 12: Distance vector algorithm
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 13: Bellman-Ford Example
u
y
z
2
2
1
3
1
1
2
5
3
5
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
Du(z) = min { cu,v + Dv(z),
cu,x + Dx(z),
cu,w + Dw(z) }
Bellman-Ford equation says:
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x
= min {2 + 5,
1 + 3,
5 + 3} = 4
node giving minimum (x) is next hop on estimated least-cost path to destination (z)

## Slide 14: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 15: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 16: Distance vector algorithm:

## Slide 17: Distance vector: example
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=0
All nodes have distance estimates to nearest neighbors (only)
A few asymmetries:
missing link
larger cost
d
e
f
a
b
c
All nodes send their local distance vector to their neighbors

## Slide 18: Distance vector example: iteration
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c

## Slide 19: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 20: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1

## Slide 21: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 22: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
8
1
2
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 23: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 24: Distance vector example: iteration
…. and so on
Let’s next take a look at the iterative computations at nodes

## Slide 25: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
b receives DVs from a, c, e
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 26: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
b receives DVs from a, c, e, computes:
a
b
c
d
e
f
DV in b:
Db(f) =2
Db(g) = ∞
Db(h) = 2
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = 2
  Db(e) = 1
e
compute
b
Db(a) = min{cb,a+Da(a), cb,c +Dc(a), cb,e+De(a)} = min{8,∞,∞} = 8
Db(c) = min{cb,a+Da(c), cb,c +Dc(c), c b,e +De(c)} = min{∞,1,∞} = 1
Db(d) = min{cb,a+Da(d), cb,c +Dc(d), c b,e +De(d)} = min{9, ∞, 2} = 2
Db(f) = min{cb,a+Da(f), cb,c +Dc(f), c b,e +De(f)} = min{∞,∞,2} = 2
Db(i) = min{cb,a+Da(i), cb,c +Dc(i), c b,e+De(i)} = min{∞, ∞, ∞} = ∞
Db(h) = min{cb,a+Da(h), cb,c +Dc(h), c b,e+De(h)} = min{∞, ∞, 2} = 2
Db(e) = min{cb,a+Da(e), cb,c +Dc(e), c b,e +De(e)} = min{∞,∞,1} = 1
Db(g) = min{cb,a+Da(g), cb,c +Dc(g), c b,e+De(g)} = min{∞, ∞, ∞} = ∞

## Slide 27: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 28: Distance vector example: computation
g
h
i
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b computes:
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
Dc(a) = min{cc,b+Db(a}} = 1 + 8 = 9
Dc(b) = min{cc,b+Db(b)} = 1 + 0 = 1
Dc(d) = min{cc,b+Db(d)} = 1+ ∞ = ∞
Dc(e) = min{cc,b+Db(e)} = 1 + 1 = 2
Dc(f) = min{cc,b+Db(f)} = 1+ ∞ = ∞
Dc(g) = min{cc,b+Db(g)} = 1+ ∞ = ∞
Dc(i) = min{cc,b+Db(i)} = 1+ ∞ = ∞
Dc(h) = min{cbc,b+Db(h)} = 1+ ∞ = ∞
DV in c:
  Dc(a) = 9
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = 2
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
compute
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 29: Distance vector example: computation
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
e receives DVs from b, d, f, h
a
b
c
DV in f:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = 0
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = 1
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
DV in h:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = ∞
  Dc(g) = 1
  Dc(h) = 0
Dc(i) = 1
DV in d:
  Dc(a) = 1
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = 0
  Dc(e) = 1
  Dc(f) = ∞ Dc(g) = 1
  Dc(h) = ∞
Dc(i) = ∞
d
e
f
g
h
i
Q: what is new DV computed in e at t=1?
compute

## Slide 30: Distance vector: state information diffusion
t=0
c’s state at t=0 is at c only
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
c’s state at t=0 has propagated to b, and may influence distance vector computations up to 1 hop away, i.e., at b
t=1
c’s state at t=0 may now influence distance vector computations up to 2 hops away, i.e., at b and now at a, e as well
t=2
c’s state at t=0 may influence distance vector computations up to 3 hops away, i.e., at b,a,e and now at c,f,h as well
t=3
c’s state at t=0 may influence distance vector computations up to 4 hops away, i.e., at b,a,e, c, f, h and now at g,i as well
t=4
Iterative communication, computation steps diffuses information through network:
t=1
t=2
t=3
t=4

## Slide 31: Network layer: “control plane” roadmap
routing protocols
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 32: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 33: Solution to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 34: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 35: Inter-AS routing: a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?

## Slide 36: Network layer: “control plane” roadmap
routing protocols
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 37: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)

## Slide 38: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 39: Network layer: “control plane” roadmap
routing protocols
Autonomous Systems
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 40: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 41: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 42: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 43: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 44: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 45: BGP path advertisement (more)
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 46: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 47: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 48: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 49: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 50: BGP: achieving policy via advertisements (more)
B
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer networks (of provider networks)
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network

## Slide 51: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w

## Slide 52: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance